Portscanner

---
Aim of the project
- Implement a portscanner in C
- Various scan methods e.g. TCP connect scan, TCP SYN scan …
- Console program like nmap

---
Implemented Scan Methods
- TCP connect scan
- TCP syn scan
- NULL scan
- XMAS scan
- FIN scan
- Maimon scan

---
TCP connect scan
- Simple approach
- Use system call connect() to try to establish a connection
- If connection successful port is open
- Else port is closed

---
Advantages/Disadvantages
- Advantages:
  + Accurate
  + Fast
  + No root privileges requires
  + Easy implementation
- Disadvantages
  - Easy detectable/logged

---
Implementation
- SOCK_STREAM socket (TCP socket)
- Use connect() function to try to establish a connection with the target machine
- Check return value of connect() function
- Return value 0 = port is open, else port closed

---
TCP Handshake

---
Syn scan
- Half-open scanning →
  doesn't open full TCP connection
- Send SYN packet
- SYN/ACK response = port is listening
- RST = port is close
- TIMEOUT(no answer) port is closed

---
Advantages/Disadvantages
- Advantages:
  + Reliable
  + Fast
  + No TCP three-way handshake → No logs
- Disadvantages
  - Requires root privileges

---
Raw socket
- receives or sends the raw datagram not including link level headers
- allows direct sending and receiving of Internet Protocol packets without any protocol-specific transport layer formatting
- Programmer builds packet to send
- Full control over headers (IP and TCP)
- Allows sophisticated scan techniques

---
Implementation
- Use RAW socket and set IP and TCP header
- Only set SYN Flag in TCP Header
- Send the packet to target machine
- Receive packets from target machine and check flags:
  - SYN/ACK flag set = port is open
  - RST flag = port is closed
  - TIMEOUT (no response) = port is filtered

---
XMAS, FIN, NULL scan
- exploits a subtle loophole in the TCP RFC to differentiate between open and closed port
- RFC 793 says:
  - “if the [destination] port state is CLOSED .... an incoming segment not containing a RST causes a RST to be sent in response”
  - If packets are sent to open ports without the SYN, RST, or ACK bits set it states: “you are unlikely to get here, but if you do, drop the segment, and return.”

---
Flags
- Null scan: Does not set any bits (TCP flag header is 0)
- FIN scan: Sets just the TCP FIN bit.
- Xmas scan: Sets the FIN, PSH, and URG flags, lighting the packet up like a Christmas tree.
- Maimon scan: Sets FIN and ACK flags

---
Implementation
- Use RAW socket and set IP and TCP header
- Set Flags depending on method in TCP Header
- Send the packet to target machine
- Try to get a response:
  - RST packet received = port is closed
  - No response = Port is open/filtered

---
Advantages/Disadvantages
- Advantages:
  + More stealthy than syn scan
  + No TCP three-way handshake → No logs
- Disadvantages
  - Requires root privileges
  - slow false positives

---
Port Scan Detector
- Aim: detect port scan of different types.
- Main Idea:
  You are (potentially) port scanned if in a short interval you receive a lot of UDP or TCP request from the same IP-Address

---
Port Scan Detector
Functionality
- A port scan is detected when a detection score of 21 points in a time range of 300ms for one individual source IP-Address is exceeded.
- Detection Score can be calculated as follows:
- Scan of a TCP destination port less than 1024: 3 points
- Scan of a TCP destination port greater or equal 1024: 1 point
- Scan of ports 11, 12, 13, 2000: 10 points
- Source https://www.sophos.com/it-it/support/knowledgebase/115153.aspx